FEATURES

- 4 bits of individually programmable IO
- 5V CMOS level outputs and 5V TTL level inputs
- Latch input values for later reading

DESCRIPTION
The HCP65 GPIO 4bit board is a general purpose input or output component with four individually programmable pins in a pseudo DIP package.

The HCP65 GPIO 4bit board is designed to interface with an 8bit microprocessors database

Pin		I/O	Function
Name	Number
5V	1, 17	Power
GND	5, 12, 21, 28	Power
Read GD	2	I	Read from data bus.
Write GD	3	I	Write to data bus.
D0	14	IO	Data bus. / Eight data lines with 3-state outputs provide a bidirectional path for data and control of the GPIO board.
D1	13
D2	11
D3	10
D4	9
D5	8
D6	7
D7	6
Enable	4	I
GPIO0	29	IO
GPIO1	27
GPIO2	22
GPIO3	20
No Connect	15, 16, 18, 19, 23, 24, 25, 26, 30, 32	NC

FUNCTIONAL BLOCK DIAGRAM

SCHEMATIC DIAGRAM